## Slide 1
TJ4S-1200-AT01 / TJ4S-1213-AT09 Riboflavin Coverage Test
1
Prepare a 0.1–0.2% riboflavin solution.
2
Spray the inner surfaces with a riboflavin spray bottle. Under a UV lamp, confirm full coverage with no shadow areas, and that the solution wets the surface as a mist.
3
After spraying, confirm the coverage under a UV lamp and photograph it with an explosion-proof phone. Include the inner wall, top head, manway, lid, spray ball, impeller, shaft, bottom, and thermowell. Attach the photos to the qualification file.
Step 3 · Photo locations
Inner wall
Top head
Manway
Lid
Spray ball
Impeller
Shaft
Bottom
Thermowell
File every location photo in the qualification record.
4
Rinse with purified water. Record rinse time, pressure, and volume.
5
After the rinse, inspect under a UV lamp. Record any riboflavin residue and where it remains. If none remains, photograph the same locations as in Step 3 and file the photos.
Step 4 · Three parameters to record
Rinse time
Rinse pressure
Rinse volume